## Slide 1: Unit 8 Loop Unrolling and Nested Loops
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
How to unroll loops in Vitis HLS
Mitigate memory bottlenecks in unrolled loops with:
  Increased memory bit width
  Memory partitioning
Design efficient nested loops

## Slide 3: Outline
Loop Unrolling and Memory Constraints
Nested Loops
FIR Filter Example

## Slide 4: Loop Unrolling
Simple idea: Repeat processing in each cycle
Unroll by 2
  Need half the number of iterations
  But double the logic

## Slide 5: Loop Unrolling in Vitis
Can be done with a simple pragma
No need to manually unroll!
Handles cases when is not divisible by unroll factor
=

## Slide 6: Memory Bottleneck
Memory bottleneck
  Loop unrolling is often limited by memory accesses
Consider vector multiply SV code
Stage 0 needs:
  Two reads from and two reads from
Stage 2 needs:
  Two writes to

## Slide 7: Single Port Memory
Recall memory architecture from Unit 4
Basic memories are single port
There is a single address decoder
Can read / write one word in a cycle
Address input bits
Address decoder Selects one of
wordlines
wordlines
Data Bus
data words
R/W

## Slide 8: Three Solutions
Solution 1: Use a true multi-port RAM
  Most general. Allows read and write from any combination of addresses
  Xilinx FGPA BRAMs are two port
  But most costly in hardware
Solution 2: Use a wider bitwidth
  Say 64 bits to read two 32 bit numbers
  Works only when the accesses are contiguous
Solution 3: Bank or partition memory
  Divide memory into partitions
  Each partition has its own decoder
  Works if accesses can be across different partitions

## Slide 9: Mutli-Port RAMs
Allow arbitrary read / writes
  Except for read-write collisions to same address in same cycle
BRAM in FPGAs generally only support true two port
BMutli-port SRAMs in ASICs are expensive
Memory
Address Decoder 2
Data1, Addr1
Address Decoder 1
Data2, Addr2

## Slide 10: Using Wider Bit widths
Wide bit width design
Only one R/W to each array
Can pipeline with II=1
But need accesses to be contiguous
Narrow bit width design
Access only one word per cycle
Memory bottleneck

## Slide 11: Mutli-Port RAMs
Allow arbitrary read / writes
  Except for read-write collisions to same address in same cycle
BRAM in FPGAs generally only support true two port
BMutli-port SRAMs in ASICs are expensive
Memory
Address Decoder 2
Data1, Addr1
Address Decoder 1
Data2, Addr2