## Slide 1: Unit 8 Shared Memory Transactions
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Describe the basic components of random access memory
  Address and data bus, address decoder, storage
Identify which types of memory should be used for storage
  External vs. internal
  Registers vs. block memory
Describe and analyze timing for the AXI4-Lite protocol for reading and writing registers
Implement a simple IP with AXI4-Lite control registers using Vitis HLS
Synthesize and simulate the IP and analyze the timing diagrams
Deploy the IP on an FPGA board and interface with the IP via PYNQ

## Slide 3: Outline
Shared Memory and Interconnects
Shared Memory Transactions
AXI4-Memory Mapped Protocol
Implementing Shared Memory in Vitis HLS

## Slide 4: Addressable Memory
An array of elements in storage
  Use for vectors, matrices, packets, data, …
Word: Each of the data element
  Typically, has word / data width = 32 or 64 bits
Memory depth = number of words
Memory size=depth word width
Address: A location of a word
  Often byte-addressable
  Word is at byte address when word width=32
Byte address
Data
0
4
8
Word 0
Word 1
Word 2
Word
Example 32-bit memory with depth

## Slide 5: Typical RAM Architecture
Three interface signals:
  Address input: Which word to select
  Read/Write: Which direction of transfer
  Data: Value to read or write
Address input:
  bits to select one of words
  Each word has a wordline select
  Selection determined by address decoder
Address input bits
Address decoder Selects one of
wordlines
wordlines
Data Bus
data words
R/W

## Slide 6: Dedicated vs Shared Memory
Dedicated memory
  Memory that is dedicated to a single hardware module
Shared memory
  Memory shared between modules
  Also processing system and peripheral I/O
Memory
Module
Memory
PS
Module 2
Module 1
Peripheral I/O

## Slide 7: Why Share Memory?
Multiple modules, I/O, PS need operate on same data
  Example video pipeline: Network I/O Filtering Coding
  Virtually all complex tasks built over multiple modules
Enables common memory for large data
  E.g., ML parameters, data, large video
  Dedicated memory becomes inefficient
Allows dynamic memory allocation
  Use memory as needed
  Allocate memory to modules as needed
Memory
PS
Module 2
Module 1
Peripheral I/O

## Slide 8: How to Build Shared Memory
Memory
Modules
Ports
Interconnect
Memory
Modules
Method 1. Multi-Port memory Each module has a dedicated port
Method 2. Interconnect
Modules use connect infrastructure

## Slide 9: Single and Multi-Port Memories
Single port
  HW module has dedicated use of a memory
  Memory has a single port
  Port exposes address, data lines with address decoder
  Does not permit transfer of data between modules
Dual or multi-port
  Multiple modules connect to the memory
  Each module has a dedicated port
  Allow simultaneous writes in same clock cycle
  Most efficient
Memory
Module
Port
Memory
Module 1
Port 1
Module 2
Port 2

## Slide 10: Problems with Multi-Port RAMs
Mutli-port SRAMs in ASICs are expensive
Typically limited to small memorys
Limited ports (e.g., 2R/2W)
Memory
Address Decoder 2
Data1, Addr1
Address Decoder 1
Data2, Addr2

## Slide 11: Interconnect
Interconnect:
  Physical and logical infrastructure for data communication
  Between two or more functional units
  Cores, memory controllers, I/O.
Topology (Physical):
  Wire layout or links (bus, mesh, crossbar, ring)
Protocol (Logical):
  Signals and timing for access (e.g., AXI4, TileLink, …)
Arbitration (Control):
  Method to resolve contention
Interconnect
Memory
Modules
Controller

## Slide 12: Transactions, Master and Slaves
Transactions:
  A transfer of data over the interconnect
Masters
  Request transactions (reads or writes)
  Ex: processors
  Kernels that need to access memory
Slaves
  Respond to transactions (reads or writes)
  Read transactions: Provide data to a master
  Write transactions: Accept data from a master
Arbiter
  Determines which transaction is used in each cycle
Interconnect
Slave 1
Master 1
Arbiter
Master
Slave

## Slide 13: Bus Topology
One data path
Only one master-pair link in each cycle
Ex: ARM AHB (Advanced High-Performance Bus)
  Pre-cursor to AXI
  Traditional shared medium
  Each master has dedicated side channel to arbiter
  Arbiter selects a master and slave based on requests
Figure from The Advanced Microcontroller Bus Architecture: An Introduction

## Slide 14: Crossbar Topology
Connects:
  masters and slaves
Supports parallel master-slave transfers
  Each master and slave can be involved in up to one transfer
  Up to transfers simultaneously
  Enables massive aggregate throughput
Masters have separate request lines
Common example: AXI4-MM protocol
  See section later

## Slide 15: Other Topologies
Ring, Mesh, NoC
Widely-used in large Systems on Chips
Advanced topic beyond this class
Figure from Chatterjee, Navonil, Suraj Paul, and Santanu Chattopadhyay. "Fault-tolerant dynamic task mapping and scheduling for network-on-chip-based multicore platform." ACM Transactions on Embedded Computing Systems (TECS) 16.4 (2017): 1-24.

## Slide 16: Outline
Shared Memory and Interconnects
Implementing Simple Transactions over Shared Memory
AXI4-Memory Mapped Protocol
Implementing Shared Memory in Vitis HLS

## Slide 17: Stream vs. Shared Memory Transactions
Dedicated stream transactions (Unit 5)
Send data & control on stream
PS
Kernel
Command stream
Control + input data
Response stream
Response + output data
Bus
IP kernel
PS
Response stream
control
Command stream
control
Data
Data
Memory
Shared memory transaction (This unit)
Send control on dedicated stream
Transfer data via shared memory

## Slide 18: Stream Transfer (Unit 5)
Consider processing system (PS) sending job to kernel
Use two streams
Command stream: PS is master and sends to kernel
  Command message descriptor
  Input data to process
Response stream: Kernel is master and sends to PS
  Processed output data
  Response descriptor (e.g., error codes, …)
PS
Kernel
Command stream
Control + input data
Response stream
Response + output data

## Slide 19: Shared Memory Transaction
PS and IP kernel both masters on a shared bus
Memory is a slave
Dedicated streams
  Command stream: PS kernel
  Response stream: Kernel PS
Streams are used for control
Right now, streams implemented on separate channels
  Ex: AXI4-Stream
  Later, we will show to map these into memory
Memory and bus are used for data
Interconnect
Memory slave
IP kernel
PS
Response stream
control
Command stream
control
Data
Data

## Slide 20: Shared Mem Transaction: Command Phase
PS writes input data into memory
  Data to be processed
PS sends input command to kernel
  Input address: Where data resides
  Output address: Where output should reside
  Command info: What to do with data
Bus
IP kernel
PS
Input command
Input data

## Slide 21: Shared Mem Transaction: Compute Phase
Kernel reads input data from memory
  Uses input address sent in command
Kernel processes input data
Bus
IP kernel
PS
Input data
Computes
results

## Slide 22: Shared Mem Transaction: Response Phase
Kernel writes output data to memory
  Uses output address sent in command
Kernel sends
Bus
IP kernel
PS
Output data
Response
Input data

## Slide 23: Streaming vs. Shared Memory
 | Streaming | Shared Memory
Access model | Sequential | Random
Control | Producer pushes data when available | Consumer pulls data when needed
Latency | Deterministic; minimal variation | Variable; depends on arbitration and usage
Arbitration | None if point-to-point | Required
Complexity |  | Simple design but adds
Resources | Dedicated resources per link, no statistical multiplexing | Shared resources, enables

## Slide 24: Streaming Example: Simple Video Processing
Deterministic sequential flow
Need dedicated high-speed links
Buffering is memory intensive
Need minimal reconfiguration
Tran, Van-Huan, and Xuan-Tu Tran. "An efficient architecture design for VGA monitor controller." 2011 International Conference on Consumer Electronics, Communications and Networks (CECNet). IEEE, 2011.

## Slide 25: Shared Memory Ex: Mobile SoC
Example:
  Qualcomm Snapdragon, Apple MacBook M3
NPU, CPU, GPU have access to common DDR memory
CPU can write address to NPU, GPU
NPU, GPU stores / retrieves data from memory
Widely-used in virtually all SoC

## Slide 26: Shared Memory Ex: Nvidia DGX H100
LLMs stored in massive shared memory
H100 GPUs fetch data as need
Use high throughput NvLink

## Slide 27: Outline
Shared Memory and Interconnects
Implementing Simple Transactions over Shared Memory
AXI4-Memory Mapped Protocol
Implementing Shared Memory in Vitis HLS

## Slide 28: AXI Family of Protocols
AXI4-Stream (Covered in Unit 5)
  Point-to-point link, flow control with TVALID / TREADY
  1 read/ write per clock cycle
  Optional framing with TLAST
AXI4-Lite (Covered in Unit 4)
  Simple memory mapped protocol. Ideal for control registers
  1 read / 1 write per 3-5 clock cycles
AXI4-Full (This unit).
  Officially called AXI4 in AMD, but we use AXI4 for the family of protocols in this class
  Builds on AXI4-Lite memory mapped
  Handshaking signals to enable high throughput 1 read / write per clock cycle
Terminology: We will use AXI-MM to mean both AXI4-Lite and AXI4-Full

## Slide 29: AXI4 Memory Mapped Features
Most widely-used interconnect fabric in industry
Multiple outstanding requests
  Master can issue several requests while others are ongoing
Full-duplex with independent read and write channels
Handshaking:
  Independent VALID/READY for requests and data and read and write.
  Provides flow control and modular design.
Out of order protocols:
  Flows marked with an ID. Order is preserved within an ID.
  But controller may rearrange packet order for different IDs enabling prioritization
Support for massive memories: DDR, HBM, not just on-chip RAM

## Slide 30: AXI4-MM Architecture
Interconnect is a crossbar
Configurable number of masters and slaves
Each master places transaction request
Crossbar typically queues requests for each slave

## Slide 31: Cost of Crossbars
Configuration | Est. Area (16nm) | Est. Gate Count (NAND2 equiv)
2 x 2 | ~0.008 mm² | ~25k - 35k
4 x 4 | ~0.035 mm² | ~100k - 140k
8 x 8 | ~0.140 mm² | ~450k - 550k
16 x 16 | ~0.600 mm² | ~2M+ (Serious congestion)
Logic cost:
  Grows with product
  But manageable relative to a large SoC
Challenge in wiring
  Wiring becomes dominant component of latency
  Metal layer exhaustion
Interconnects often 30-40% area in large SoCs
Logic estimates for AXI crossbar
64-bit address and data in TSMC 16 nm
How data flows is key to high throughput design

## Slide 32: Review: AXI4-Lite Write Protocol
Suppose master wants to write data to address
  AWADDR= and AWVALID=1
  WDATA= and WVALID=1
  Both can occur in independent clock cycles
When slave is ready for address or data it sets:
  AWREADY=1 and WREADY=1
  Slave can set these independently and any time it is ready
Transfer:
  When AWREADY=AWVALID=1 together address is transferred
  When WREADY=WVALID=1 together data is transferred
Handshake:
  After both are transferred, slave set BREADY=1
  Master sets BVALID=1 to acknowledge
  Can start next transaction in same clock cycle as BVALID=1
AWREADY
AWADDR, AWVALID
BVALID
WDATA, WVALID
WREADY
BREADY
MASTER
SLAVE

## Slide 33: AXI4-Full Burst Signals
AXI4-Full supports bursts of data
  1 cycle per read / write
  Much faster than AXI4-Lite (typically 3-5 cycles)
Additional signals sent on request:
  AxLEN: Number of “beats” to transfer
  AxSIZE: Width of transfer (for downward compatibility)
  AxBURST: Type of burst (fixed or increment address)
Transfer stage: Unchanged
  Same WDATA, WVALID, WREADY
Termination: Add WLAST
  Indicates final beat (can terminate for AWLEN)
AWREADY
AWADDR, AWVALID
BVALID
WDATA, WVALID
WREADY
BREADY
MASTER
SLAVE
AWLEN, AWSIZE, AWBURST
WLAST

## Slide 34: AXI4 Write Example
Two write burst requests
  Burst 0: AWLEN=0
  Burst 1: AWLEN=5
Request 1 early
  Before write burst 0 completed
WLAST at end of each burst

## Slide 35: AXI4 Indexing
Each transaction associated with an index
Index is not unique
Typical design:
  Each master has a unique ID; or
  One ID for priority class
Crossbar will maintain order within an ID
But may re-order between IDs
Can be used for prioritization
Advanced topic

## Slide 36: Outline
Shared Memory and Interconnects
Implementing Simple Transactions over Shared Memory
AXI4-Memory Mapped Protocol
Implementing Shared Memory in Vitis HLS

## Slide 37: Two Memory Interfaces in Vitis
Native:
  Typically used for direct connection to internal memories
  Synthesized with a simple address decoder
  Word indexed
  Supported in Vivado with BRAM
AXI4-MM
  Typically used for DRAM or BRAM on a bus
  Kernel connects to AXI4 memory controller (a block in Vivado)
  AXI4-MM is always byte addressed

## Slide 38: BRAM
Creates native interface to BRAM
AXI4-Lite
  Read and write pointer
  Length n
Can read from memory in kernel

## Slide 39: BRAM TB
Creates BRAM emulation
  Or actual memory

## Slide 40: AXI4 Histogram Example
Non-uniform histogram
Given:
  data values
  bin edges
Compute
  ,
  Includes underflow and overflow values

## Slide 41: Histogram Command Input
Gives input addresses:
  Data
  Bin edges
Output addresses
  Counts
Transaction IDs and lengths

## Slide 42: Histogram Interface
AXI4 streams
  For command and response
  These could have been memory-mapped
AXI4-Full access to memory
Read command from AXI4 stream

## Slide 43: Histogram Read Phase
Read data and bin edges to a local buffer
Local buffer is not strictly needed for data
  Easy to illustrate

## Slide 44: Core Histogram Loop
Nested loop
Outer loop is not pipelined
Must be careful of inner loop pipelining
Will show synthesis reports in class

## Slide 45: Testbench Memory Allocation
Testbench creates memory
Allocates blocks in memory
Computes byte addresses

## Slide 46: Testbench Command
Writes addresses in command
Upon receipt of response
  Retieves data
  Compares against test vectors

## Slide 47: Timing: Read Phases
Test parameters
  7 bins
  37 data points
Partitioning
  Data broken into three busts
  16, 16, and 5
  Requests given at beginning