## Slide 1: Unit 10 Arrays and Matrix Multiplications
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Estimate compute and memory operations for basic matrix operations
  Determine which operations are compute or data-limited
Describe how to store and address matrices in sequential memory
  Row-major and column-major
Implement simple baseline multiplication with loop unrolling
  Implement using Vitis pragmas
  Estimate cost
Recognize high fanout computations
Implement and describe cycle-to-cycle behavior of systolic arrays
Implement and estimate timing for tiled matrix multiplication

## Slide 3: Outline
Matrix Multiplications
Hardware Implementation via Broadcast
Systolic Arrays
Tiling for Large Matrices

## Slide 4: What is a Matrix?
An array of numbers
Rows x columns
Many applications
Data matrix
  Ex: Each row is a set of values of a sample
Image
  Each entry is a pixel
Time series
  Each row is a time step
  Each column is some attribute that changes over time

## Slide 5: Matrix Addition and Subtraction
and must be the same size
  Can be rectangular
Simply add elements:
From Khan Academy. Excellent review of matrix math if you need it

## Slide 6: Matrix Addition Complexity
Suppose
Reading : each matrix
  elements per interface word
Computation multiplications
Writing :
Complexity dominated by reading and writing
  Called data-limited
  Not compute limited
Parallelizing additions does not help significantly
  Unless matrices are already loaded

## Slide 7: Matrix Multiplication
Basic operation in range of fields
Machine learning
Communications
Robotics
…
Virtually every mathematical field

## Slide 8: Multiplying Two Matrices
From excellent Medium post
A Complete Beginners Guide to Matrix Multiplication for Data Science with Python Numpy

## Slide 9: Storing Matrices in Hardware Memory
Typically stored in RAM
SRAM / BRAM for internal memory
  Smaller matrices or portions of matrices
DRAM for external memory
  Larger / complete memory
Often stored in row-major order
  Store first row
  Store second row
  …

## Slide 10: Row-Major Order in Memory
Suppose is stored in row-major order
Consider neighboring elements in the same row
  Eg.
These elements are contiguous
If you have a wide memory bit width
  Can access neighboring elements in the same column
  But cannot access elements in neighboring rows

## Slide 11: Matrix Multiplication Complexity
Matrix multiplication formula:
Need MAC operations
  MAC = multiply and accumulate
Complexity grows quickly

## Slide 12: Multiplication Memory Accesses
Read and
  reads
Write
  writes
Can read / write words per cycle
  memory bit width
  word bit width
Typically compute dominates
Thus matrix multiplication needs efficient compute

## Slide 13: Sample Problem

## Slide 14: Outline
Matrix Multiplications
Hardware Implementation via Broadcast
Systolic Arrays
Tiling for Large Matrices

## Slide 15: Naïve Implementation in Vitis
Classic triple nested loop
Takes iterations
Simple, but slow
How can we speed this up?

## Slide 16: Problem 1: No Parallelism
Triple loop requires cycles
Only one multiply per cycle
Resource efficient
But slow
We could try to unroll
That is, do multiplications in parallel
But…

## Slide 17: Problem 2: Array Accesses
Each inner iteration requires
  Read from and
  Write to
Access are from random locations
Unroll requires parallel accesses

## Slide 18: Two Assumptions
We can obtain a better multiplication under two key assumptions
Assumption 1: can be stored in register
  That is, fully partitioned memory
  Typically, must be small
Assumption 2: and admit row-wise access
  That is, can access all elements of a row in parallel
  Matrices must be in internal memory
  Different columns are in different memory banks
  Or external memory but very wide data width
We will relax both assumptions later with tiling

## Slide 19: Memory Partitioning in Vitis
Partition and row-wise
  All elements of each row can be accessed in parallel
Fully partition
  All elements of can be accessed in parallel

## Slide 20: Local Row Buffers
Create row buffers
  Store each row of and
Fully partition row buffers

## Slide 21: Pipeline Loop
Three stages
Load row of
  All loads are in parallel
Compute
  All MACs are in parallel
  Note double UNROLL pragma
Store row
  All are in parallel

## Slide 22: Best Case Complexity
Each pipeline has three stages
  Latency = 3
  II = 1
Complexity: Cycles =
Storage:
  stored in banks of each
  stored in banks of each
  stored in registers
MAC units:

## Slide 23: Baseline Implementation Summary
Conclusion: Baseline implementation achieves
  Dramatic speed up
  Enables highly parallel MACs
But there are two problems:
Problem 1: Local storage:
  Requires local storage and partitioned arrays
  We will address this with tiling
Problem 2: Complex routing
  We will discuss and address this next

## Slide 24: Outline
Matrix Multiplications
Hardware Implementation via Broadcast
Systolic Arrays
Tiling for Large Matrices

## Slide 25: Baseline Implementation Layout
Consider the layout of baseline multiplier
Row buffer for
Row buffer for
Matrix
Row of ( elements)
Row of ( elements)

## Slide 26: Routing Challenges: Fanout
Each must be broadcast
  To locations
We say the fanout of is
High fanout is hard to route
Creates large number of wires
Many wires can be long
Difficult to meet timing

## Slide 27: Simple Example
Consider simple example to left
Parameter is broadcast
  To instances of function
Fanout is

## Slide 28: Fanout Visualized
Fanout is

## Slide 29: Reduced Fan-Out Design
Improved design with lower fanout
Copy in a shift register
  Takes cycles
  And additional registers
Use a delay line
  Shift in one element of at a time
Use copy of in each function

## Slide 30: Reduced Fan-Out Visualized
Fan-out is reduced from to 2
Computations can be local
Key lesson: Add additional delay and register
But greatly improve routing

## Slide 31: Systolic Arrays
See slides from Prof Sai Zhang
Provided to NYU students on Brightspace

## Slide 32: Outline
Matrix Multiplications
Hardware Implementation via Broadcast
Systolic Arrays
Tiling

## Slide 33: Memory Bottleneck
Suppose matrices and can only be read one word per cycle
Reading and writing take cycles
If we have systolic array:
  Computation take s cycles
So, memory, not computation is the bottleneck

## Slide 34: Block Matrices
Partition a matrix into sub-matrices or blocks
Full matrix
Matrix blocks
Block matrix form

## Slide 35: Tiling for Matrix Multiplication
Divide rows in tiles of size
  and will have block rows
  will have block rows
Divide columns in tiles of size
  and will have block columns
  will have block columns
Systolic array will be

## Slide 36: Tiling Procedure
Load full matrix into local memory once
  Let block
For each block row
  Load rows of and into local memory
  Perform matrix multiplications via systolic arrays
  Performed for and
  Complexity of each block matrix multiplication is
  So, cost is